## Slide 1
Where to locate a solar plant in Chile?

## Slide 2
Where to locate a solar plant in Chile?
Let’s review the video “Solar Energy in Chile”.
Notes: *Note : If you have downloaded the video to your computer, you can edit the presentation to generate a hyperlink to the video from this slide.

## Slide 3
Según el video, ¿qué factores afectan la producción y distribución de energía eléctrica de las plantas solares?
Where to locate a solar plant in Chile?
Why is it important to consider solar energy as an alternative to provide electricity?
What factors affect the production and distribution of electrical energy generated by solar plants, according to what is indicated in the video?

## Slide 4
Problem
What would be the best place to locate a solar plant that delivers electricity to Concepción: the Atacama Desert or the surroundings of Concepción?

## Slide 5
Problem
What would be the best place to locate a solar plant that delivers electricity to Concepción: the Atacama Desert or the surroundings of Concepción?
What does it take to make the decision?

## Slide 6
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%

## Slide 7
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%
Inicial amount

## Slide 8
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%
This power is reduced before reaching the solar panel's surface due to the atmosphere's humidity, which varies between Atacama and Concepción.

## Slide 9
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%
Energy is measured in kWh (kilowatt hours), corresponding to the multiplication of power measured in kW by the number of hours.

## Slide 10
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%
It is desired to compare the amount of electrical energy that reaches Concepción from each solar plant daily.

## Slide 11
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%
The panels cannot convert all of the energy received into electrical energy since 80% of it is dissipated as thermal energy.

## Slide 12
Available Information
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%
In the case of the Atacama plant, part of the electrical energy produced is lost when transmitted to Concepción due to the resistance of the cables that carry it.

## Slide 13
Now that we have this data, is it possible to determine which is the most convenient place to locate the solar plant?
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%

## Slide 14
Let's work on the following questions:
Calculate the power that reaches the solar panel on each plant, considering what is lost due to the humidity of the atmosphere.
Activity

## Slide 15
The sun's power that reaches each Atacama plant solar panel is 1,4 ∙ 0,46 = 0,644 kW.
The sun's power that reaches each solar panel at the Concepción plant is 1,4 ∙ 0,39 = 0,546 kW.
1. Calculate the power that reaches the solar panel on each plant, considering what is lost due to the humidity of the atmosphere.
Activity

## Slide 16
One way to measure energy is in kWh (kilowatt hours). If there are 12 hours of sunshine per day on each plant, how much energy reaches the panel daily on a sunny day on each plant?
Activity

## Slide 17
One way to measure energy is in kWh (kilowatt hours). If there are 12 hours of sunshine per day on each plant, how much energy reaches the panel daily on a sunny day on each plant?
Activity
To a solar panel in Atacama, they arrive daily 0,644 ∙ 12 = 7,728 kWh of energy.
While 0,546 ∙ 12 = 6,552 kWh of energy arrives daily at a solar panel in Concepción.

## Slide 18
How much energy (kWh) reaches a solar panel in a year, considering the number of days with sun on each plant?
A solar panel in Atacama annually receives 7,728 ∙ 349 = 2 697,072 kWh of energy.
A solar panel in Concepción annually receives 6,552 ∙ 296 = 1 939,392 kWh of energy.
Activity

## Slide 19
How much energy (kWh) reaches a solar panel on average per day in each plant?
Activity
An average of 2 697,072: 365 ≈ 7,389 kWh of energy reaches a solar panel in Atacama per day.
An average of 1 939,392: 365 ≈ 5,313 kWh of energy reaches a solar panel in Concepción per day.

## Slide 20
Activity
5. Of the average daily amount of energy that reaches the panel calculated in the previous question, how much does it arrive as electrical energy to Concepción from each plant?

## Slide 21
Activity
5. Of the average daily amount of energy that reaches the panel calculated in the previous question, how much does it arrive as electrical energy to Concepción from each plant?
Considering heat loss and other effects:
A solar panel in Atacama produces 7,389 ∙ 0,2 = 1,478 kWh of electrical energy daily.
A solar panel in Concepción produces 5,313 ∙ 0,2 = 1,063 kWh of electrical energy daily.

## Slide 22
Considering the energy loss in the cables:
A solar panel in Atacama can transmit to Concepción 1,478 ∙ 0,91 = 1,344 kWh of electrical energy per day.
A solar panel in Concepción supplies its city with 1,063 kWh of electricity per day.
5. Of the average daily amount of energy that reaches the panel calculated in the previous question, how much does it arrive as electrical energy to Concepción from each plant?
Activity

## Slide 23
A solar plant in Atacama can produce more electrical energy than a plant in Concepción. However, the humidity loss in energy production and the transmission loss from Atacama to Concepción makes it necessary to compare the amount of energy that reaches this city from each plant.
Conclusions

## Slide 24
To obtain the daily amount of electrical energy that can be supplied to Concepción from a solar panel located in Atacama and another in the city of Concepción itself, we had to perform a series of calculations that involved rational numbers.
Conclusions

## Slide 25
We obtained the best location for the solar plant from the available information. Other variables could affect the production and distribution of energy from each of these solar plants.
Conclusions
 | Plant in Atacama | Plant in Concepción
Power if the Sun per m2 on the external surface of the atmosphere | 1,4 kW | 1,4 kW
Percentage of light that is absorbed by humidity before reaching the solar panel | 54% | 61%
Hours of sunshine per day | 12 | 12
Sunny days per year | 349 | 296
Percentage of light that is lost in the panel in heat and other effects | 80% | 80%
Percentage of energy lost in transmission cables | 9% | 0%

## Slide 26
Where to locate a solar plant in Chile?